Invitation to Quote (ITQ)

Procurement For goods under Shopping:  Laboratory Equipment and Glassware for two final beneficiaries, located in Moldova: Scientific-Practical Institute of Horticulture and Food Technologies (ISPHTA) and Agro-Industrial College „Gheorghe Răducan” from Grinauti village (GRINAUTI).

Project Title: Fruit Garden Project (EIB financed).

Contracting Authority: Consolidated Unit for Implementing & Monitoring the Wine Sector Restructuring Program (UCIMPRSVV).

Date: 18 June, 2021

ITQ No: # LAB_GRINAUTI_ISPHTA_2021

Attention to: Laboratory Equipment and Laboratory Glassware Suppliers

Dear Suppliers of laboratory equipment and glassware,

you are invited to submit your bids to supply laboratory equipment and glassware for the laboratory rooms of the following two final beneficiaries, located in Moldova: Scientific-Practical Institute of Horticulture and Food Technologies (ISPHTA - Institutul Stiintifico-Practic de Horticultura si Tehnologii Alimentare, or. Codru, str.Vieru 59, MD-2070, Chisinau, R.Moldova) and Agro-Industrial College „Gheorghe Raducan” from Grinauti village (GRINAUTI). Supply period is up to 2 months from contract award date. The Bidder must bid for 100% of requested items for both beneficiaries (this Shopping is not divided into lots).

Notes on Technical Specifications:

- The Purchaser requires that all goods and materials to be incorporated in the goods to be new, unused, and of the most recent or current models, and that they incorporate all recent improvements in design and materials, unless provided for otherwise in the ITQ.

- The bid must be supported by manufacturer’s technical data leaflets or readable photocopies/pictures clearly commented for each of the items and technical parameters offered.

- The Bids must comply with the minimum requested technical specifications indicated in the below tables. Major technical non-compliance(s) – if so considered by Purchaser, shall lead to rejection of the bid. Incomplete quantities, types of goods (incomplete bids) shall lead to rejection of the bid.

- The Bidder must complete the technical table(s) below, indicating for each of the lines below - the offered technical specification; brand/manufacturer, model name/number

The following goods (with minimum technical parameters) are requested to be delivered and fully installed at ISPHTA:

| № | Description of goods | Minimum Requested technical parameters | Unit | Qty |
| --- | --- | --- | --- | --- |
| 1 | Echipament analize ELISA - Micro-Plate Washer | Intended Use: ELISA Micro-Plate Washer Plate: 96 well and strips; Residual Volume: ≤2ul; Dispensing volume: Adjustable from at least 50 ul to 900 ul or more; Wash cycles: from 1 up to 9 or more; Soak time: adjustable up to 15 min or more; Shake time: adjustable up to 15 min or more; Display: LCD Buffer or reagent selection: automated switching for up to 3 buffers or more; | pcs | 1 |
|  | Echipament analize ELISA - Micro-plate Reader | Intended Use: ELISA Micro-plate Reader For 96 well plate Light source: Halogen lamp; Filters: 405nm, 450nm, 490nm, 630nm or more; OD Accuracy: ±1% (0.000-2.000Abs) or better; Wavelength Range: from at least 405 up to 630 nm or wider; Display: LCD USB ports for printer and PC connection Software: Microplate Reader and Imager included. | pcs | 1 |
|  | Laminar Flow Cabinet | Intended Use: for sterile work External Size (W*D*H): 1300*750*1850mm (±150mm); Airflow Velocity: Average of 0.3~0.5m/s; Pre-filter: from 4 up to 30 um or better; HEPA Filter: 99% efficiency at 0.3um Lamp: 12-35W*1 or 5-16W LED UV Lamp: 15-30W*1 (±10W) or 15-30 W LED Power Supply: AC220V±10%, 50/60Hz | pcs | 2 |

The following goods (with minimum technical parameters) are requested to be delivered and fully installed at GRINAUTI Agro industrial College:

| No | Description of goods (Minimum Requested technical parameters) | Cant. Buc/set |
| --- | --- | --- |
| 1 | PAHAR BERZELIUS FORMA JOASA 150 ML Pahar Berzelius forma joasa Gradat, cu cioc Material: sticla borosilicata Capacitate: 150 ml Diametru: 60 mm Inaltime: 82 mm Confom DIN 12331, ISO 3819 | 5 |
| 2 | PAHAR ERLENMEYER GAT LARG 150 ML Pahar Erlenmeyer gat larg Cu gradatii Material: sticla borosilicata Capacitate: 150 ml Diametru baza: 72 mm Inaltime: 120 mm Diametru gura:50 mm Cf DIN 12385 | 5 |
| 3 | BIURETA 25 ML CU ROBINET DREPT DIN STICLA Biureta cu robinet Material: sticla Cf ISO 385 Certificat de lot Capacitate: 25 ml Acuratete: ± 0,05 ml Gradatie: 0,1 ml Gradatie : 560 mm | 3 |
| 4 | VAS DE CRISTALIZARE CU CIOC 1000 ML Vas de cristalizare cu cioc Material: sticla borosilicata 3.3 Capacitate: 1000 ml Diametru: 150 mm Inaltime: 75 mm | 1 |
| 5 | PIPETA GOLIRE TOTALA 15 ML CLASA A Pipeta gradata cu golire totala clasa A Cod culoare Cf ISO 1769, ISO 835 Gradatie normala Certificat de lot Capacitate: 15 ml Acuratete: ± 0,08 ml Gradatie: 0,1 ml Timp scurgere : 9 - 19 secunde Cod culoare: portocaliu | 3 |
| 6 | MOJAR CU PISTIL 100 ML Mojar cu pistil Material: portelan de inalta calitate Include mojarul si pistilul Capacitate: 100 ml Diametru exterior: 90 mm Diametru interior: 75 mm Inaltime: 48 mm | 3 |
| 7 | CILINDRU GRADAT 10 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 10 ml Acuratete: ± 0,10 ml Gradatie: 0,2 ml | 5 |
| 7.1 | CILINDRU GRADAT 25 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 25 ml Acuratete: ± 0,25 ml Gradatie: 0,5 ml | 5 |
| 7.2 | CILINDRU GRADAT 50 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 50 ml Acuratete: ± 0,50 ml Gradatie: 1 ml | 5 |
| 7.3 | CILINDRU GRADAT 100 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 100 ml Acuratete: ± 0,50 ml Gradatie: 1 ml | 5 |
| 7.4 | CILINDRU GRADAT 250 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 250 ml Acuratete: ± 1 ml Gradatie: 2 ml | 5 |
| 8 | EPRUBETA 5 ML 12/75 MM Eprubeta fara margine Material: neutral glass Capacitate: 5 ml Diametru: 12 mm Lungime: 75 mm Grosime perete: 0,8-1 mm Set 250 buc. | 1 set |
| 8.1 | EPRUBETA 8,5 ML 13/100 MM Eprubeta fara margine Material: neutral glass Capacitate: 8,5 ml Diametru: 13 mm Lungime: 100 mm Grosime perete: 0,8-1 mm Set 250 buc. | 1 set |
| 8.2 | EPRUBETA 13 ML 16/100 MM Eprubeta fara margine Material: neutral glass Capacitate: 13 ml Diametru : 16 mm Lungime : 100 mm Grosime perete: 1-1,2 mm Set 100 buc. | 1 set |
| 8.3 | EPRUBETA 19 ML 16/150 MM Eprubeta fara margine Material : neutral glass Capacitate : 19 ml Diametru : 16 mm Lungime : 150 mm Grosime perete : 1,0-1,2 mm Set 100 buc. | 1 set |
| 8.4 | EPRUBETA 43 ML 20/200 MM Eprubeta fara margine Material : neutral glass Capacitate : 43 ml Diametru : 20 mm Lungime : 200 mm Grosime perete : 1,0-1,2 mm Set 100 buc. | 1 set |
| 9 | PALNIE FILTRARE TIJA SCURTA Ø 50 MM Palnie de filtrare Diametru: 50 mm Lungime tija: 50 mm Diametru tija: 7 mm Material: sticla borosilicata, conform ISO 4798 | 3 |
| 10 | SPIRTIERA 120 ML CAPAC STICLA Spirtiera confenctionata din sticla Include un fitil Model: cu capac de sticla nefiletabil si garnitura de metal fixa Capacitate: 120 ml | 10 |
| 11 | SPATULA CU LINGURA 150 MM OTEL INOX Spatula cu lingura Lungime : 150 mm Material : otel inox | 1 |
| 12 | PENSETA VARF ASCUTIT Penseta varf foarte ascutit, foarte puternic Lungime: 120 mm Material: otel inox | 1 |
| 12.1 | PENSETA CU VARF LAT Penseta varf lat, pentru lucru cu materiale plate Lungime : 110 mm Material : otel inox | 1 |
| 12.2 | PENSETE PENTRU LAMELE SI MEMBRANE Penseta pentru lamele si membrane Lungime : 115 mm Material : otel inox | 1 |
| 12.3 | PENSETA CU VARF SUBTIRE CURBAT Penseta cu varf subtire curbat Lungime: 130 mm Material: otel inox | 1 |
| 13 | CLEMA TREI DEGETE AJUSTARE DUBLA 0-35 MM CU MUFA Clema cu trei degete imbracate in PVC cu mufa Ajustare dubla Diametru: 0 - 35 mm | 5 |
| 14 | SET 9 PERII Set din 9 perii Pentru uz general Contine perii (nylon sau par natural) pentru majoritatea aplicatiilor din laborator | 1 set |
| 15 | AEROMETRE Set care sa contina : 1 aerometru 1.200-1.420 g/cm3 1 aerometru 1.020-1220 g/cm3 1 aerometru 1400-1620 g/cm3 | 1 set |
| 16 | ANSE CALIBRATE 1 MICROLITRU Anse insamantare Material: HIPS HIPS: High Impact Polystyrene Forma hexagonala Sterile Capacitate: 1 microlitru Culoare: alb Impachetare: 1 bucata/pachet Set 500 buc. | 5 set |
| 17 | LAME MICROSCOP MARGINI TAIATE Lame microscop cu margini taiate Unghi: 90° Material: sticla clara, precuratata Dimensiuni 26x76 mm Grosime: 1,0-1,2 mm Impachetate in cutii de carton cu folie celofan dubla protectoare intre fiecare lame Set 50 buc. | 3 set |
| 17.1 | LAMELE MICROSCOP 24x24 MM Lamele microscop Material: sticla precuratata Ambalate in cutie de plastic, protejata in folie de aluminiu Grosime : 0,13-0,16 mm Dimensiuni: 24x24 mm Set 200 buc. | 3 set |
| 18 | PLACI PETRI STICLA 60 MM Placi Petri 60 mm Material: soda lime glass Diametru: 60 mm Inaltime: 15 mm | 15 |
| 19 | AUTOCLAV Volum minim: 20 litri | 1 |
| 20 | BAIE DE APA TERMOSTATATA Baie de apa termostatata Carcasa metalica Strucutura metalica la exterior acoperita cu un strat epoxy (tratament anti rugina) Interior din otel inox Control digital al temperaturii: 5°C peste temperatura camerei ...99°C sau mai mult Rezolutie: 1°C Functionare continua sau cu posibilitatea de programare cu semnal acustic sau vizual dla terminarea programului setat Timer: 1....999 minute sau mai mult Display digital : temperatura si timp Semnal acustic sau vizual petru supraincalzire Include: cos, capac cu gauri si reductiile: 8 si 5-6 cm Capacitate minimă: 3 litri | 1 |
| 21 | MICROSCOP DIGITAL Microscop bionocular, inclinare 300 , rotabil 3600 Operare fara cabluri folosing acumulator Li-Ion reincarcabil Oculare 10X /18mm Livrat cu 4 obiective : 4 x, 10 x, 40 X si 100X Iluminare LED cel putin 1W Modul digital minim 3,2MPx Port USB , Software dedicat transfer si analiza imagini | 1 |
| 22 | LUPA Diametru 90mm marire minim 2,5X | 1 |
| 23 | CENTRIFUGA Posibilitate de programare si operare pentru a obtine o precizie ridicata cu controlul vitezei Viteza poate fi setata si afisata prin RPM sau G-force de la 300 rpm pana la 4500 rpm /2490xg sau mai mult Rotorul inclus pentru utilizarea cu tuburi: de dimensiuni 12 buc.x10 ml si 8 buc x15 ml. Motor: fara perii Turatie: 300 - 4500 RPM sau mai mult Rezolutie turatie: 100 RPM Timp accelerare/franare: accelerare - 20 sec franare - 13 sec RCF maxim: 2490xg sau mai mult Cronometru: 1 -99 minute sau (HOLD) functionare continua Certificari: CE, Adaptor si conector pentru tuburi incluse după necesitate | 1 |
| 24 | FRIGIDER LABORATOR Frigider de laborator Domeniu temperatura: 0...8 ºC sau mai larg Capacitate minimă: 150 litri Dimensiuni exterioare: minim 600x600x825 mm Usa – material solid Stabilitate temperatura: nu mai mare de ± 2 ºC Uniformitate temperatura: mai putin de 3 ºC Display pentru vizualizare Control digital al temperaturii cu o precizie de 0,1 ºC 3 tipuri de alarme (cresterea sau scaderea temperaturii, defectarea senzorului de temperatura si pentru usa deschisa) Echipata cu 3 rafturi, ajustabile in inaltime Dimensiuni rafturi: minim 460x400 mm Iluminare LED si blocare Interior/exterior: oțel inox /otel galvanizat cu acoperire | 1 |
| 25 | CAMERA DE NUMARARE DE TIP HEMOCIMETRU | 1 |
| 26 | INCUBATOR COMPACT TERMOSTATAT CU VENTILATIE NATURALA Incubație sigură și reproductibilă chiar și în condiții de operare continua Atmosferă stabilă prin ușa interioară din sticlă Interval de temperatură: +5 °C TC până la +80 °C Capacitate / Volum util: 15-20 litri. | 1 |
| 27 | DULAP PENTRU REACTIVI Dulap - stocare chimicale: acizi si baze - dulap, realizat din otel de minim 8/10 mm grosime, acoperit de vopsea epoxidica, aplicata electrostatic, prevazut cu 2 usi si 3 rafturi ajustabile pe înălțime, din oțel zincat vopsit cu pulberi epoxidice; bazin colector la partea inferioara; rafturi în formă de tavă pentru colecatrea lichidelor; sistem de inchidere automata a usii. Dimensiuni externe minim 600/500/1690 mm si dimensiuni la interior approx 530/463/1533. In concordanta cu normele EN 61010-1, EN 14727; marcaj CE | 1 |
| 28 | LAMPA ULTRAVIOLETA Lămpile bactericide sunt utilizate pentru dezinfecția aerului și a suprafețelor prin intermediul radiației UV-C. Datorită luminii cu ultraviolete lampa sterilizează în mod eficient microorganismele dăunătoare sănătații: bacterii, virusuri, mucegaiul, etc. Tip: recirculator bactericid Numărul de becuri: 2 Tehnologie: raze ultraviolete Carcasă: metal Suprafata maximală, m2: 30 Circulația aerului, m³/h: 85 | 2 |
| 29 | TAVA/CUVA COLORARE SCHIEFERDECKER Tava/cuva colorare cu capac Schieferdecker Material: neutral glass Pentru 10 lame de microscop | 1 |
| 30 | TERMOMETRU -10-110 GRADE Termometru -10 - 110ºC Fara mercur Cu lichid colorat Domeniu de temperatura: -10..110ºC Acuratete: 1 ºC Lungime: 300 mm Diametru: 6 mm | 1 |
| 31 | ETUVA CONVECTIE FORTATA Etuva cu convectie fortata 45-65 litri Exterior: carcasa metalica vopsita (rasina epoxidica ) Interior din otel inox Temperatura ajustabila intre : ambiant +10ºC - 300 ºC Rezolutie: nu mai mare de 1 ºC Stabilitate temperatura : nu mai mult de ±1ºC Reglarea temperaturii se face cu ajutorul microprocesorului Functii : protectie la supraincalzire, , operare la o temperatura fixa, reglarea timpului : 0-9999 minute, corectarea deviatiei, Omogenitate temperatura : nu mai mult de ±2,5 ºC Picioare reglabile pentru a facilita instalarea Usa este prevazuta cu geam , rezistent la temperaturi inalte Convectie fortata Livrat cu doua rafturi ajustabile pe inaltime Numarul maxim de rafturi: 47 | 1 |
| 32 | Mediu Nutritiv Agar agar 1 Kg + Peptona 1 Kg | 1 set |

Full delivery by Supplier, under this contract, is requested (loading/unloading/sorting the goods in distinct, separate packages – indicating the destination name of beneficiary). Partial deliveries shall not be accepted. The Purchaser shall collect on its premises/warehouse the full order per beneficiary and perform one full delivery for ISPHTA and one full delivery for GRINAUTI.

2.	You must bid for all the items under this tender. Bids will be evaluated for all the items and contracts awarded to the firm offering the lowest evaluated total cost of all the requested items under this shopping. Incomplete (on list items and/or quantities and/or adjacent installation services) bids shall be disqualified. The contracting Authority reserves the right to modify original quantities by +/- 20%.

3.	 Your bid, in the form attached (Attachment 1 to this ITQ) (together with the following necessary documents: Copy of the company’s registration certificate, documentary proof on financial and qualification requirements) must be submitted in a sealed envelope at the following address:

Consolidated Unit for Implementing & Monitoring the Wine Sector Restructuring Program (UCIMPRSVV),18 Calea Basarabiei str., 2nd floor, off.9 Chisinau, Republic of Moldova, MD-2023

Attn: Iurie Brumarel, Executive Director of UCIMPRSVV

4.	 Your quotation in English or Romanian language, should be accompanied by adequate detailed technical documentation for each item quoted. The company shall provide catalogue(s) and other printed similar materials or pertinent information (in English or Romanian or Russian language) for items quoted.

5.	 The deadline for receipt of your bid by the Purchaser at the address indicated in Paragraph 3 is: hour 10:00 AM, July 06, 2021.

6. 	Bids by fax or by electronic means are not acceptable.

7.	You bid should be submitted as per the following instructions and in accordance with the attached Contract (for Contract Form see Attachment 2 to this ITQ).

(i) PRICES: Prices can be quoted in EUR or MDL.

(ii) EVALUATION OF BIDS:  Offers determined to be substantially responsive to the technical specifications will be evaluated by comparison of their prices by converting their price to the Moldovan Leu (MDL) based on the official exchange rate published by the National Bank of Moldova on the date specified in Paragraph 5 of this invitation for submission of quotations.

In evaluating the quotations, the Purchaser will determine for each proposal the evaluated price by adjusting the price quotation by making any correction for any arithmetical errors as follows:

(a) where there is a discrepancy between amounts in figures and in words, the amount in words will govern;

(b) where is a discrepancy between the unit rate and the line item total resulting from multiplying the unit rate by the quantity, the unit rate as quoted will govern;

If a Supplier refuses to accept the correction, its bid will be rejected.

(iii) AWARD OF CONTRACT: The award will be made to the bidder offering the lowest evaluated price and that meets the required standards of technical and financial capabilities. The successful bidder will sign a Contract as per attached form of contract and terms and conditions of supply/performance.

(iv) VALIDITY OF THE OFFER: Your quotation(s) should be valid for a period of sixty (60) days from the deadline for receipt of bid indicated in Paragraph 5 of this ITQ.

(v) DELIVERY and INSTALLATION TERMS: Delivery period is set not later than 2 months from contract signing date.

8. 	Further information can be obtained from:

PIU Procurement Officer,

Consolidated Unit for Implementing & Monitoring the Wine Sector Restructuring Program (UCIMPRSVV)

Tel/Fax: (+373) 22 260906; oleg.lipcean@winemoldova.md

9.	Please Confirm by Fax/ E-mail the receipt of this invitation and whether or not you will submit the price quotation(s).

10. The prices quoted by the Bidder shall not be subject to adjustment during the performance of the Contract. Note: The goods and services that are procured under Finance Contract no (Serapis) 2014-0041, signed between the Government of the Republic of Moldova and the European Investment Bank, are free of import taxes, VAT and payment of customs duties according to Government of Moldova Decision nr. 246 from 08 April 2010 (Published in the official gazette Monitorul Oficial al Republicii Moldova, from 2017, nr. 73-77 art.195).

11.	Limitation of damages/loss:

This ITQ does not constitute an offer. No agreement shall result upon submission of proposals/bids. The Project/Contracting Authority SHALL NOT BE UNDER ANY OBLIGATION TO ENTER INTO ANY AGREEMENT WITH ANYONE IN CONNECTION WITH THIS ITQ unless the Project/Contracting Authority executes and delivers an agreement in writing approved by the Project/Contracting Authority.

By submitting a proposal, the Bidder agrees that in no event will the Bidder claim damages in excess of an amount equivalent to the reasonable costs incurred by the Bidder in preparing its proposal for matters relating to any agreement or concerning the competitive process, and, the Bidder, by submitting a proposal, waives any claim for loss of profits if no agreement is made with the Bidder.

The Project/Contracting Authority reserves the right to reject any and all bids (including the lowest cost proposal); The Project/Contracting Authority reserves the right to cancel this tender at any time for any reasons (with or without commencing a new tender process in its place).

Sincerely,

Iurie BRUMAREL

UCIMPRSVV Executive Director

Attachment 1.

{include your company’s letterhead}

Terms and Conditions of Supply

Project Name: Fruit Garden of Moldova

Contracting Authority/Purchaser:	 Consolidated Unit for Implementing & Monitoring the Wine Sector Restructuring Program (UCIMPRSVV)

Dear Sirs,

As per your Invitation to Quote (# LAB_GRINAUTI_ISPHTA_2021), we are pleased to submit the present Bid as follows:

1.	Prices and Schedules for Delivery:

The following goods are offered to be supplied and installed at ISPHTA:

| Line Item N( | Description of Goods | Physical unit | Quantity | Unit PRICE per line item / (currency / valuta) | TOTAL PRICE per line item / (currency / valuta) | Delivery (as per Incoterms) from contract signing date |
| --- | --- | --- | --- | --- | --- | --- |
|  | Echipament analize ELISA - Micro-Plate Washer | pcs | 1 |  |  | 8 weeks |
|  | Echipament analize ELISA - Micro-plate Reader | pcs | 1 |  |  | 8 weeks |
|  | Laminar Flow Cabinet | pcs | 2 |  |  | 8 weeks |
| TOTAL PRICE, ISPHTA (currency / valuta) |  |  |

Note: In case of discrepancy between unit price and Total derived from unit price, unit price shall prevail.

All prices must be indicated 0% VAT and free of any other taxes.

The following goods are offered to be supplied and installed at GRINAUTI College:

| Line Item N( | Description of Goods | Physical unit | Quantity | Unit PRICE per line item / (currency / valuta) | TOTAL PRICE per line item / (currency / valuta) | Delivery (as per Incoterms) from contract signing date |
| --- | --- | --- | --- | --- | --- | --- |
|  | PAHAR BERZELIUS FORMA JOASA 150 ML | pcs | 5 |  |  | 8 weeks |
|  | PAHAR ERLENMEYER GAT LARG 150 ML | pcs | 6 |  |  | 8 weeks |
|  | BIURETA 25 ML CU ROBINET DREPT DIN STICLA | pcs | 3 |  |  | 8 weeks |
|  | VAS DE CRISTALIZARE CU CIOC 1000 ML | pcs | 1 |  |  | 8 weeks |
|  | PIPETA GOLIRE TOTALA 15 ML CLASA A | pcs | 3 |  |  | 8 weeks |
|  | MOJAR CU PISTIL 100 ML | pcs | 3 |  |  | 8 weeks |
|  | CILINDRU GRADAT 10 ML CLASA A | pcs | 5 |  |  | 8 weeks |
| 7.1 | CILINDRU GRADAT 25 ML CLASA A | pcs | 5 |  |  | 8 weeks |
| 7.2 | CILINDRU GRADAT 50 ML CLASA A | pcs | 5 |  |  | 8 weeks |
| 7.3 | CILINDRU GRADAT 100 ML CLASA A | pcs | 5 |  |  | 8 weeks |
| 7.4 | CILINDRU GRADAT 250 ML CLASA A | pcs | 5 |  |  | 8 weeks |
|  | EPRUBETA 5 ML 12/75 MM (250 buc) | set | 1 |  |  | 8 weeks |
| 8.1 | EPRUBETA 8,5 ML 13/100 MM (250 buc) | set | 1 |  |  | 8 weeks |
| 8.2 | EPRUBETA 13 ML 16/100 MM (100 buc) | set | 1 |  |  | 8 weeks |
| 8.3 | EPRUBETA 19 ML 16/150 MM (100 buc) | set | 1 |  |  | 8 weeks |
| 8.4 | EPRUBETA 43 ML 20/200 MM (100 buc) | set | 1 |  |  | 8 weeks |
|  | PALNIE FILTRARE TIJA SCURTA Ø 50 MM | pcs | 3 |  |  | 8 weeks |
|  | SPIRTIERA 120 ML CAPAC STICLA | pcs | 10 |  |  | 8 weeks |
|  | SPATULA CU LINGURA 150 MM OTEL INOX | pcs | 1 |  |  | 8 weeks |
|  | PENSETA VARF ASCUTIT | pcs | 1 |  |  | 8 weeks |
| 12.1 | PENSETA CU VARF LAT | pcs | 1 |  |  | 8 weeks |
| 12.2 | PENSETE PENTRU LAMELE SI MEMBRANE | pcs | 1 |  |  | 8 weeks |
| 12.3 | PENSETA CU VARF SUBTIRE CURBAT | pcs | 1 |  |  | 8 weeks |
|  | CLEMA TREI DEGETE AJUSTARE DUBLA 0-35 MM CU MUFA | pcs | 5 |  |  | 8 weeks |
|  | SET 9 PERII | set | 1 |  |  | 8 weeks |
|  | AEROMETRE | set | 1 |  |  | 8 weeks |
|  | ANSE CALIBRATE 1 MICROLITRU | set | 5 |  |  | 8 weeks |
|  | LAME MICROSCOP MARGINI TAIATE | set | 3 |  |  | 8 weeks |
| 17.1 | LAMELE MICROSCOP 24x24 MM | set | 3 |  |  | 8 weeks |
|  | PLACI PETRI STICLA 60 MM | pcs | 15 |  |  | 8 weeks |
|  | AUTOCLAV | pcs | 1 |  |  | 8 weeks |
|  | BAIE DE APA TERMOSTATATA | pcs | 1 |  |  | 8 weeks |
|  | MICROSCOP DIGITAL | pcs | 1 |  |  | 8 weeks |
|  | LUPA | pcs | 1 |  |  | 8 weeks |
|  | CENTRIFUGA | pcs | 1 |  |  | 8 weeks |
|  | FRIGIDER LABORATOR | pcs | 1 |  |  | 8 weeks |
|  | CAMERA DE NUMARARE DE TIP HEMOCIMETRU | pcs | 1 |  |  | 8 weeks |
|  | INCUBATOR COMPACT TERMOSTATAT CU VENTILATIE NATURALA | pcs | 1 |  |  | 8 weeks |
|  | DULAP PENTRU REACTIVI | pcs | 1 |  |  | 8 weeks |
|  | LAMPA ULTRAVIOLETA | pcs | 2 |  |  | 8 weeks |
|  | TAVA/CUVA COLORARE SCHIEFERDECKER | pcs | 1 |  |  | 8 weeks |
|  | TERMOMETRU -10-110 GRADE | pcs | 1 |  |  | 8 weeks |
|  | ETUVA CONVECTIE FORTATA | pcs | 1 |  |  | 8 weeks |
|  | Mediu Nutritiv | set | 1 |  |  | 8 weeks |
| TOTAL PRICE, GRINAUTI (currency / valuta) |  |  |

Note: In case of discrepancy between unit price and Total derived from unit price, unit price shall prevail.

All prices must be indicated 0% VAT and free of any other taxes.

----------------------------------------------------------------------------------------------------------

TOTAL Bid Price (ITQ # LAB_GRINAUTI_ISPHTA_2021 / ISPHTA+GRINAUTI) =

{indicate total bid price in numbers and figures}

----------------------------------------------------------------------------------------------------------

2.	Fixed Price The prices indicated above are firm and fixed and not subject to any adjustment during contract performance. Final order quantities may be adjusted by Purchaser with +/-20%.

3.	Delivery Schedule: The delivery and full installation should be completed within 8 weeks since the date of contract signing. Note: all goods procured shall be new, and never used before.

4.	Payment For local Suppliers (residents of Moldova), payment for Goods and Services shall be made in MD Lei at the official exchange rate of the EUR to the MDL, fixed by the National Bank of Moldova from the date of fiscal bill issue. Payment for your invoice will be made within 10 calendar days.

5.	Warranty: 12 months for the supplied new equipment since acceptance (by Beneficiary) date.

- Delivery, Packaging and Marking Instructions:

Glassware shall be transmitted to Final User(s) when 100% of supply quantity for a certain final user is gathered at the Supplier’s warehouse. Partial deliveries are not accepted.

Goods shall be grouped in boxes, per type of equipment and glassware and per distinct Beneficiary. Boxes will bear the marks: Name of Beneficiary / name of goods (and line number per contract) / quantities in the box.

- Failure to Perform: The Purchaser may cancel the Contract if the Supplier fails to deliver the Goods and Services, in accordance with the above terms and conditions, in spite of a 21 day notice given by the Purchaser, without incurring any liability to the Supplier.

- Technical Requirements:

Attachment 2 to this ITQ

(# LAB_GRINAUTI_ISPHTA_2021)

Covenant of Integrity to UCIMPRSVV from the Supplier:

“We declare and covenant that neither we nor anyone, including any of our directors, employees or agents, acting on our behalf with due authority or with our knowledge or consent, or facilitated by us, has engaged, or will engage, in any Prohibited Practice (as defined below) in connection with the tendering process or in the execution or supply of any works, goods or services for this ITQ (the “Contract”) and covenant to so inform you if any instance of any such Prohibited Practice shall come to the attention of any person in our organization having responsibility for ensuring compliance with this Covenant. We shall, for the duration of the tender process and, if we are successful in our tender, for the duration of the Contract, appoint and maintain in office an officer, who shall be a person reasonably satisfactory to you and to whom you shall have full and immediate access, having the duty, and the necessary powers, to ensure compliance with this Covenant. If (i) we have been, or any such director, employee or agent acting as aforesaid has been, convicted in any court of any offence involving a Prohibited Practice in connection with any tendering process or provision of works, goods or services during the five years immediately preceding the date of this Covenant, or (ii) any such director, employee or agent has been dismissed or has resigned from any employment on the grounds of being implicated in any Prohibited Practice, we give details of that conviction, dismissal or resignation below, together with details of the measures that we have taken, or shall take, to ensure that neither this company nor any of our directors, employees or agents commits any Prohibited Practice in connection with the Contract. In the event that we are awarded the Contract, we grant the Project Owner, the European Investment Bank (EIB) and auditors appointed by either of them, as well as any authority having competence under European Union law, the right of inspection of our records. We accept to preserve these records generally in accordance with applicable law but in any case for at least six years from the date of substantial performance of the Contract.” For the purpose of this Covenant,

• “Corrupt Practice” means the offering, giving or promising of any improper advantage to influence the action of a Public Official, or the threatening of injury to his person, employment, property, rights or reputation, in connection with any procurement process or in the execution of any contract in order that any person may obtain or retain business improperly or obtain any other improper advantage in the conduct of business.

• “Fraudulent Practice” means a dishonest statement or act of concealment which is intended to, or tends to, influence improperly the procurement process or the execution of a contract to the detriment of the Project Owner, or is designed to establish tender prices at non-competitive levels and to deprive the Project Owner of the benefits of fair and open competition, and includes collusive practices (whether before or after tender submission) among tenderers or between a tenderer and a consultant or a representative of the Project Owner.

• “Project Owner“ means the person designated as such in the tender documents or the Contract.

• “Public Official” means any person holding a legislative, administrative, managerial, political or judicial post in any country, or exercising any public function in any country; or a director or employee of a public authority or of a legal person controlled by a public authority of any country; or a director or official of a public international organization.

• “Prohibited Practice“ means an act that is a Corrupt Practice or a Fraudulent Practice.

NAME OF THE SUPPLIER____________________________________________________

Authorized Signature__________________________________________________________

Place:		        	          Date:

Attachment 2.

ITQ # LAB_GRINAUTI_ISPHTA_2021

Technical Specifications

- The Purchaser requires that all goods and materials to be incorporated in the goods to be new, unused, and of the most recent or current models, and that they incorporate all recent improvements in design and materials, unless provided for otherwise in the ITQ.

- The bid must be supported by manufacturer’s technical data leaflets or readable photocopies/pictures clearly commented for each of the items and technical parameters offered.

- The Bids must comply with the minimum requested technical specifications indicated in the below tables. Major technical non-compliance(s) – if so considered by Purchaser, shall lead to rejection of the bid. Incomplete quantities, types of goods (incomplete bids) shall lead to rejection of the bid.

- The Bidder must complete the technical table(s) below, indicating for each of the lines below - the offered technical specification, brand/manufacturer, model name/number

The following goods (with minimum technical parameters) are requested to be delivered and fully installed at ISPHTA:

| № | Description of goods | Minimum Requested technical parameters | Unit | Qty |
| --- | --- | --- | --- | --- |
| 1 | Echipament analize ELISA - Micro-Plate Washer | Intended Use: ELISA Micro-Plate Washer Plate: 96 well and strips; Residual Volume: ≤2ul; Dispensing volume: Adjustable from at least 50 ul to 900 ul or more; Wash cycles: from 1 up to 9 or more; Soak time: adjustable up to 15 min or more; Shake time: adjustable up to 15 min or more; Display: LCD Buffer or reagent selection: automated switching for up to 3 buffers or more; | pcs | 1 |
| 2 | Echipament analize ELISA - Micro-plate Reader | Intended Use: ELISA Micro-plate Reader For 96 well plate Light source: Halogen lamp; Filters: 405nm, 450nm, 490nm, 630nm or more; OD Accuracy: ±1% (0.000-2.000Abs) or better; Wavelength Range: from at least 405 up to 630 nm or wider; Display: LCD USB ports for printer and PC connection Software: Microplate Reader and Imager included. | pcs | 1 |
| 3 | Laminar Flow Cabinet | Intended Use: for sterile work External Size (W*D*H): 1300*750*1850mm (±150mm); Airflow Velocity: Average of 0.3~0.5m/s; Pre-filter: from 4 up to 30 um or better; HEPA Filter: 99% efficiency at 0.3um Lamp: 12-35W*1 or 5-16W LED UV Lamp:15-30W*1 (±10W) or 15-30 W LED Power Supply: AC220V±10%, 50/60Hz | pcs | 2 |

The following goods (with minimum technical parameters) are requested to be delivered and fully installed at GRINAUTI:

| No | Description of goods (Minimum Requested technical parameters) | Cant. Buc/set |
| --- | --- | --- |
| 1 | PAHAR BERZELIUS FORMA JOASA 150 ML Pahar Berzelius forma joasa Gradat, cu cioc Material: sticla borosilicata Capacitate: 150 ml Diametru: 60 mm Inaltime: 82 mm Confom DIN 12331, ISO 3819 | 5 |
| 2 | PAHAR ERLENMEYER GAT LARG 150 ML Pahar Erlenmeyer gat larg Cu gradatii Material: sticla borosilicata Capacitate: 150 ml Diametru baza: 72 mm Inaltime: 120 mm Diametru gura:50 mm Cf DIN 12385 | 5 |
| 3 | BIURETA 25 ML CU ROBINET DREPT DIN STICLA Biureta cu robinet Material: sticla Cf ISO 385 Certificat de lot Capacitate: 25 ml Acuratete: ± 0,05 ml Gradatie: 0,1 ml Gradatie : 560 mm | 3 |
| 4 | VAS DE CRISTALIZARE CU CIOC 1000 ML Vas de cristalizare cu cioc Material: sticla borosilicata 3.3 Capacitate: 1000 ml Diametru: 150 mm Inaltime: 75 mm | 1 |
| 5 | PIPETA GOLIRE TOTALA 15 ML CLASA A Pipeta gradata cu golire totala clasa A Cod culoare Cf ISO 1769, ISO 835 Gradatie normala Certificat de lot Capacitate: 15 ml Acuratete: ± 0,08 ml Gradatie: 0,1 ml Timp scurgere : 9 - 19 secunde Cod culoare: portocaliu | 3 |
| 6 | MOJAR CU PISTIL 100 ML Mojar cu pistil Material: portelan de inalta calitate Include mojarul si pistilul Capacitate: 100 ml Diametru exterior: 90 mm Diametru interior: 75 mm Inaltime: 48 mm | 3 |
| 7 | CILINDRU GRADAT 10 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 10 ml Acuratete: ± 0,10 ml Gradatie: 0,2 ml | 5 |
| 7.1 | CILINDRU GRADAT 25 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 25 ml Acuratete: ± 0,25 ml Gradatie: 0,5 ml | 5 |
| 7.2 | CILINDRU GRADAT 50 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 50 ml Acuratete: ± 0,50 ml Gradatie: 1 ml | 5 |
| 7.3 | CILINDRU GRADAT 100 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 100 ml Acuratete: ± 0,50 ml Gradatie: 1 ml | 5 |
| 7.4 | CILINDRU GRADAT 250 ML CLASA A Cilindru gradat clasa A Material: sticla borosilicata Cf ISO 4788 si USP ''Batch number'' printat pe cilindru Certificat pe lot Capacitate: 250 ml Acuratete: ± 1 ml Gradatie: 2 ml | 5 |
| 8 | EPRUBETA 5 ML 12/75 MM Eprubeta fara margine Material: neutral glass Capacitate: 5 ml Diametru: 12 mm Lungime: 75 mm Grosime perete: 0,8-1 mm Set 250 buc. | 1 set |
| 8 | EPRUBETA 8,5 ML 13/100 MM Eprubeta fara margine Material: neutral glass Capacitate: 8,5 ml Diametru: 13 mm Lungime: 100 mm Grosime perete: 0,8-1 mm Set 250 buc. | 1 set |
| 8.1 | EPRUBETA 13 ML 16/100 MM Eprubeta fara margine Material: neutral glass Capacitate: 13 ml Diametru : 16 mm Lungime : 100 mm Grosime perete: 1-1,2 mm Set 100 buc. | 1 set |
| 8.2 | EPRUBETA 19 ML 16/150 MM Eprubeta fara margine Material : neutral glass Capacitate : 19 ml Diametru : 16 mm Lungime : 150 mm Grosime perete : 1,0-1,2 mm Set 100 buc. | 1 set |
| 8.4 | EPRUBETA 43 ML 20/200 MM Eprubeta fara margine Material : neutral glass Capacitate : 43 ml Diametru : 20 mm Lungime : 200 mm Grosime perete : 1,0-1,2 mm Set 100 buc. | 1 set |
| 9 | PALNIE FILTRARE TIJA SCURTA Ø 50 MM Palnie de filtrare Diametru: 50 mm Lungime tija: 50 mm Diametru tija: 7 mm Material: sticla borosilicata, conform ISO 4798 | 3 |
| 10 | SPIRTIERA 120 ML CAPAC STICLA Spirtiera confenctionata din sticla Include un fitil Model: cu capac de sticla nefiletabil si garnitura de metal fixa Capacitate: 120 ml | 10 |
| 11 | SPATULA CU LINGURA 150 MM OTEL INOX Spatula cu lingura Lungime : 150 mm Material : otel inox | 1 |
| 12 | PENSETA VARF ASCUTIT Penseta varf foarte ascutit, foarte puternic Lungime: 120 mm Material: otel inox | 1 |
| 12.1 | PENSETA CU VARF LAT Penseta varf lat, pentru lucru cu materiale plate Lungime : 110 mm Material : otel inox | 1 |
| 12.2 | PENSETE PENTRU LAMELE SI MEMBRANE Penseta pentru lamele si membrane Lungime : 115 mm Material : otel inox | 1 |
| 12.3 | PENSETA CU VARF SUBTIRE CURBAT Penseta cu varf subtire curbat Lungime: 130 mm Material: otel inox | 1 |
| 13 | CLEMA TREI DEGETE AJUSTARE DUBLA 0-35 MM CU MUFA Clema cu trei degete imbracate in PVC cu mufa Ajustare dubla Diametru: 0 - 35 mm | 5 |
| 14 | SET 9 PERII Set din 9 perii Pentru uz general Contine perii (nylon sau par natural) pentru majoritatea aplicatiilor din laborator | 1 set |
| 15 | AEROMETRE Set care sa contina : 1 aerometru 1.200-1.420 g/cm3 1 aerometru 1.020-1220 g/cm3 1 aerometru 1400-1620 g/cm3 | 1 set |
| 16 | ANSE CALIBRATE 1 MICROLITRU Anse insamantare Material: HIPS HIPS: High Impact Polystyrene Forma hexagonala Sterile Capacitate: 1 microlitru Culoare: alb Impachetare: 1 bucata/pachet Set 500 buc. | 5 set |
| 17 | LAME MICROSCOP MARGINI TAIATE Lame microscop cu margini taiate Unghi: 90° Material: sticla clara, precuratata Dimensiuni 26x76 mm Grosime: 1,0-1,2 mm Impachetate in cutii de carton cu folie celofan dubla protectoare intre fiecare lame Set 50 buc. | 3 set |
| 17.1 | LAMELE MICROSCOP 24x24 MM Lamele microscop Material: sticla precuratata Ambalate in cutie de plastic, protejata in folie de aluminiu Grosime : 0,13-0,16 mm Dimensiuni: 24x24 mm Set 200 buc. | 3 set |
| 18 | PLACI PETRI STICLA 60 MM Placi Petri 60 mm Material: soda lime glass Diametru: 60 mm Inaltime: 15 mm | 15 |
| 19 | AUTOCLAV Volum minim: 20 litri | 1 |
| 20 | BAIE DE APA TERMOSTATATA Baie de apa termostatata Carcasa metalica Strucutura metalica la exterior acoperita cu un strat epoxy (tratament anti rugina) Interior din otel inox Control digital al temperaturii: 5°C peste temperatura camerei ...99°C sau mai mult Rezolutie: 1°C Functionare continua sau cu posibilitatea de programare cu semnal acustic sau vizual dla terminarea programului setat Timer: 1....999 minute sau mai mult Display digital : temperatura si timp Semnal acustic sau vizual petru supraincalzire Include: cos, capac cu gauri si reductiile: 8 si 5-6 cm Capacitate minimă: 3 litri | 1 |
| 21 | MICROSCOP DIGITAL Microscop bionocular, inclinare 300 , rotabil 3600 Operare fara cabluri folosing acumulator Li-Ion reincarcabil Oculare 10X /18mm Livrat cu 4 obiective : 4 x, 10 x, 40 X si 100X Iluminare LED cel putin 1W Modul digital minim 3,2MPx Port USB , Software dedicat transfer si analiza imagini | 1 |
| 22 | LUPA Diametru 90mm marire minim 2,5X | 1 |
| 23 | CENTRIFUGA Posibilitate de programare si operare pentru a obtine o precizie ridicata cu controlul vitezei Viteza poate fi setata si afisata prin RPM sau G-force de la 300 rpm pana la 4500 rpm /2490xg sau mai mult Rotorul inclus pentru utilizarea cu tuburi: de dimensiuni 12 buc.x10 ml si 8 buc x15 ml. Motor: fara perii Turatie: 300 - 4500 RPM sau mai mult Rezolutie turatie: 100 RPM Timp accelerare/franare: accelerare - 20 sec franare - 13 sec RCF maxim: 2490xg sau mai mult Cronometru: 1 -99 minute sau (HOLD) functionare continua Certificari: CE, Adaptor si conector pentru tuburi incluse după necesitate | 1 |
| 24 | FRIGIDER LABORATOR Frigider de laborator Domeniu temperatura: 0...8 ºC sau mai larg Capacitate minimă: 150 litri Dimensiuni exterioare: minim 600x600x825 mm Usa – material solid Stabilitate temperatura: nu mai mare de ± 2 ºC Uniformitate temperatura: mai putin de 3 ºC Display pentru vizualizare Control digital al temperaturii cu o precizie de 0,1 ºC 3 tipuri de alarme (cresterea sau scaderea temperaturii, defectarea senzorului de temperatura si pentru usa deschisa) Echipata cu 3 rafturi, ajustabile in inaltime Dimensiuni rafturi: minim 460x400 mm Iluminare LED si blocare Interior/exterior: oțel inox /otel galvanizat cu acoperire | 1 |
| 25 | CAMERA DE NUMARARE DE TIP HEMOCIMETRU | 1 |
| 26 | INCUBATOR COMPACT TERMOSTATAT CU VENTILATIE NATURALA Incubație sigură și reproductibilă chiar și în condiții de operare continua Atmosferă stabilă prin ușa interioară din sticlă Interval de temperatură: +5 °C TC până la +80 °C Capacitate / Volum util: 15-20 litri. | 1 |
| 27 | DULAP PENTRU REACTIVI Dulap - stocare chimicale: acizi si baze - dulap, realizat din otel de minim 8/10 mm grosime, acoperit de vopsea epoxidica, aplicata electrostatic, prevazut cu 2 usi si 3 rafturi ajustabile pe înălțime, din oțel zincat vopsit cu pulberi epoxidice; bazin colector la partea inferioara; rafturi în formă de tavă pentru colecatrea lichidelor; sistem de inchidere automata a usii. Dimensiuni externe minim 600/500/1690 mm si dimensiuni la interior approx 530/463/1533. In concordanta cu normele EN 61010-1, EN 14727; marcaj CE | 1 |
| 28 | LAMPA ULTRAVIOLETA Lămpile bactericide sunt utilizate pentru dezinfecția aerului și a suprafețelor prin intermediul radiației UV-C. Datorită luminii cu ultraviolete lampa sterilizează în mod eficient microorganismele dăunătoare sănătații: bacterii, virusuri, mucegaiul, etc. Tip: recirculator bactericid Numărul de becuri: 2 Tehnologie: raze ultraviolete Carcasă: metal Suprafata maximală, m2: 30 Circulația aerului, m³/h: 85 | 2 |
| 29 | TAVA/CUVA COLORARE SCHIEFERDECKER Tava/cuva colorare cu capac Schieferdecker Material: neutral glass Pentru 10 lame de microscop | 1 |
| 30 | TERMOMETRU -10-110 GRADE Termometru -10 - 110ºC Fara mercur Cu lichid colorat Domeniu de temperatura: -10..110ºC Acuratete: 1 ºC Lungime: 300 mm Diametru: 6 mm | 1 |
| 31 | ETUVA CONVECTIE FORTATA Etuva cu convectie fortata 45-65 litri Exterior: carcasa metalica vopsita (rasina epoxidica ) Interior din otel inox Temperatura ajustabila intre : ambiant +10ºC - 300 ºC Rezolutie: nu mai mare de 1 ºC Stabilitate temperatura : nu mai mult de ±1ºC Reglarea temperaturii se face cu ajutorul microprocesorului Functii : protectie la supraincalzire, , operare la o temperatura fixa, reglarea timpului : 0-9999 minute, corectarea deviatiei, Omogenitate temperatura : nu mai mult de ±2,5 ºC Picioare reglabile pentru a facilita instalarea Usa este prevazuta cu geam , rezistent la temperaturi inalte Convectie fortata Livrat cu doua rafturi ajustabile pe inaltime Numarul maxim de rafturi: 47 | 1 |
| 32 | Mediu Nutritiv Agar agar 1 Kg + Peptona 1 Kg | 1 set |

Full delivery by Supplier, under this contract, is requested (loading/unloading/sorting the goods in distinct, separate packages -– indicating the destination name of beneficiary). Partial deliveries shall not be accepted. The Purchaser shall collect on its premises/warehouse the full order per beneficiary and perform one full delivery for ISPHTA and one full delivery for GRINAUTI College.

Attachment 3.

{model} CONTRACT

Contract Nr.	# LAB_GRINAUTI_ISPHTA_2021					Data:____ iulie, 2021

Numele ofertantului:

ADRESA:

Tel.

Email:

Reprezentată de

“Furnizor”, pe de o parte,

ŞI

„Unitatea consolidată pentru implementarea şi monitorizarea Programului de

restructurare a sectorului vitivinicol” (UCIMPRSVV)

Adresa Oficiului:  mun. Chisinau, str.Calea Basarabiei 18, et.2 (MD-2023)

Tel:(+373) 260901; 069176027; 078812200; fax: 260912, Email: iurie.brumarel@winemoldova.md

Reprezentat de Iurie Brumarel, Director Executiv,

“Cumpărător”, pe de altă parte, au încheiat următorul contract:

1. SUBIECTUL CONTRACTULUI

Furnizorul se angajează să livreze şi Cumpărătorul se angajează să procure bunurile şi serviciile indicate în specificaţiile Contractului „BUNURI” (Anexa 1)  în termenii şi condiţiile stipulate de prezentul Contract. Acest contract este valabil pina la 31/12/2021.

2. CALITATEA BUNURILOR

Calitatea Bunurilor trebuie să corespundă Specificaţiilor Tehnice indicate în Anexa 1 si Anexa 2 a prezentului Contract.

- PREŢUL CONTRACTULUI

3.1. Preţurile BUNURILOR sunt stabilite în {valuta} şi indicate în specificaţia Contractului.

3.2. Suma totală a Contractului este {suma}.

- TERMENII ŞI CONDIŢIILE DE LIVRARE

4.1 FURNIZORUL va livra BUNURILE si Serviciile incidente in termeni conform Anexa 1. Livrarea/prestarea se face la adresa/beneficiari finali:

- Institutul Stiintifico-Practic de Horticultura si Tehnologii Alimentare, str.Vieru 59, MD-2070, Chisinau, R.Moldova;

- Colegiul Agro-Industrial „Gheorghe Răducan” din satul Grinauti, R.Moldova;

4.2 BUNURILE vor fi însoţite de următoarele documente:

- Lista de inventar (Act(e) primire-predare);

- Factura, semnată şi ştampilată;

- Certificat de garanție pentru bunurile livrate;

4.3 Furnizorul este responsabil pentru vamuire. Dacă Cumpărătorul este scutit de plata TVA si altor taxe, el trebuie să prezinte la Vamă documente relevante. Furnizorul este responsabil să anunţe Cumpărătorul în avans (5 zile lucrătoare) despre necesitatea de a pregăti şi prezenta documentele necesare la vamă.

4.4 Dacă termenii de livrare nu sunt respectaţi, FURNIZORUL va plăti pagubele în mărime de 0.5% din preţul fiecărei unităţi a BUNURILOR pentru fiecare zi de întârziere şi până la 10 % din suma Contractului stabilită în p.  3.2 mai sus.

5. PLATA

CUMPĂRĂTORUL efectuează plata pentru „BUNURI” (Anexa 1), in MDL la rata oficiala de schimb EUR/MDL stabilita de către Bancă Naționala a Moldovei la ziua eliberarii facturii fiscale, in modul următor:

- 70% (saptezeci procente) din suma contractului (confirmat prin act de predare primire 100% cantitate per Beneficiar, semnate de Cumparator si Beneficiarul Final), în termen de 10 zile lucrătoare, in baza facturii fiscale eliberate de către FURNIZOR, in {valuta}.

-  plata finala, 30% (treizeci procente) din suma contractului, în termen de 10 zile lucrătoare din ziua acceptarii calitatii tuturor bunurilor livrate, de catre Cumparator si Beneficiar final, in baza facturii fiscale eliberate de Furnizor.

6. CONDIŢIILE ACCEPTĂRII BUNURILOR

Acceptarea în cazul prezentului Contract înseamnă prezentarea de către FURNIZOR a unui set complet de documente de expediţie şi a unui protocol de acceptare din partea CUMPĂRĂTORULUI. Orice costuri la care va fi supus CUMPĂRĂTORUL din cauza documentelor incorecte remise de FURNIZOR, se vor face din contul celui din urmă.

7. GARANŢIA

7.1 BUNURILE furnizate trebuie să aibă un termen de garanţie in conformitate cu Anexa 1 a rezentului Contract.

7.2 Serviciile de Garanţie vor fi efectuate de Furnizor.

7.3 Dacă pe parcursul termenului de garanţie indicat în p. 7.1 orice BUNURI se vor defecta din cauza modelării greşite, materialelor sau a factorului uman, FURNIZORUL (la discreţie) va repara sau va înlocui acestea gratuit, cu condiţia că acestea nu au fost modificate sau reparate de altcineva, au fost depozitate conform recomandărilor FURNIZORULUI şi că acestea au fost întoarse FURNIZORULUI sau reprezentantului autorizat de către acesta împreună cu nota originală de ambalare şi motivele de restituire.

8. ARBITRARE

8.1 Toate disputele care pot să apară în legătură cu prezentul Contract vor fi aplanate prin negocieri de către Părţile implicate.

8.2 Dacă Părţile nu pot soluţiona disputa sau neînţelegerile din timpul negocierilor, atunci aşa dispută va fi adresată pentru analiză şi aplanare instantei de judecata, in conformitate cu legislatia Rep. Moldova.

8.3 Acest Contract se va supune legilor Republicii Moldova.

9. FORŢELE MAJORE

Partile se scutesc de răspundere pentru ne-îndeplinirea parţiala sau totala a obligaţiilor conform prezentului Contract daca a intervenit o forţa majora : avarie, incendiu, inundaţii sau cutremur de pământ, război, acte nelegitime ale terţelor persoane in funcţii, intrarea in vigoare a actelor legale de interzicere directa sau indirecta a activităţilor, ce pot împiedica derularea prezentului Contract, ce pot provoca in general lichidarea Părţilor ca persoane juridice sau a altor circumstanţe ce au apărut după semnarea prezentului Contract ce nu depind de buna voinţa a Părţilor. In acest caz termenii de îndeplinire a obligaţiilor conform prezentului Contract se vor deplasa proporţional timpului pe parcursul căruia au existat forte majore. In caz ca aceste circumstanţe funcţionează mai mult de 3 (trei) luni, părţile au dreptul de a rezilia prezentul Contract si nici una din Părţi nu va avea dreptul de a cere careva compensaţii pentru pierderi de la Partea opusa. Faptul de intervenire sau dispariţie a situaţiei Forţele Majore se va confirma de un act legal emis de un organ autorizat de stat.

10 ALŢI TERMENI ŞI CONDIŢII

10.1 Orice schimbări sau amendamente la prezentul Contract vor intra în forţă doar când vor fi făcute în formă scrisă şi semnate de reprezentanţi autorizaţi ai ambelor Părţi. Toate amendamentele şi anexele constituie o parte integrantă a prezentului Contract, în cazul în care sunt făcute în formă corectă.

10.2 Dacă se consemnează de ambele Părţi, un item din Anexa 1 poate fi înlocuit de un altul egal sau mai ieftin decât cel care se înlocuieşte, cu condiţia că acesta este echivalent din punct de vedere tehnic sau chiar superior celui înlocuit.

10.3 Prezentul Contract este făcut în două originale identice în limba romana.

10.4 Contractul intră în vigoare din data semnării lui de către Părţi, şi este valid până la sfârşitul tuturor condiţiilor de garanţie, de plată sau a celor stipulate de prezentul Contract. Termenii Contractului pot fi prelungiţi, stopaţi pentru o perioadă de timp sau chiar anulaţi în baza unui acord mutual al Părţilor.

10.5 Prezentul Contract este compus din următoarele documente:

- Contractul dat;

- Specificaţiile prezentului Contract (Anexa 1 si Anexa 2);

| Furnizor: ADRESA: Tel. Email: Contul Furnizorului: Cod fiscal: Numele băncii: Adresa băncii: Codul băncii: | Cumparatorul: Unitatea consolidata pentru implementarea şi monitorizarea Programului de restructurare a sectorului vitivinicol” (UCIMPRSVV) Adresa juridica: bd. Stefan cel Mare 162 Cod fiscal: 1010601000302 Banca: MF-TT Chisinau-bugetul de stat IBAN: _______________________________ Prestatorul platitor: MF-Trezoreria de Stat Codul bancii: TREZMD2X |
| --- | --- |

FURNIZORUL						CUMPĂRĂTORUL

Iurie Brumarel

Director Executiv

Anexa 1 la Contractul Nr. # LAB_GRINAUTI_ISPHTA_2021

Livrabile :

(copia ofertei)

| Nr | Name of Goods | Measurement Unit | Quantity | Unit PRICE per line item / (currency / valuta) | TOTAL PRICE per line item / (currency / valuta) | Expected delivery time from contract signing date |
| --- | --- | --- | --- | --- | --- | --- |
| Beneficiary name |
|  |  |  |  |  |  | 8 weeks |
| TOTAL PRICE (currency / valuta) |  |  |

*Preturile sunt indicate la cota 0% TVA.

**Costul livrarii bunurilor (incarcare/descarcare), este inclus in costul bunurilor.

| Furnizor: ADRESA: Tel. Email: Contul Furnizorului: Cod fiscal: Numele băncii: Adresa băncii: Codul băncii: | Cumparatorul: Unitatea consolidata pentru implementarea şi monitorizarea Programului de restructurare a sectorului vitivinicol” (UCIMPRSVV) Adresa juridica: bd. Stefan cel Mare 162 Cod fiscal: 1010601000302 Banca: MF-TT Chisinau-bugetul de stat IBAN: ______________________________ Prestatorul platitor: MF-Trezoreria de Stat Codul bancii: TREZMD2X |
| --- | --- |

FURNIZORUL						CUMPĂRĂTORUL

Iurie Brumarel

Director Executiv

Anexa 2 la contractul # LAB_GRINAUTI_ISPHTA_2021

Specificatii Tehnice

(copia ofertei)